## Slide 1: The Arduino life
Workshop on Arduino Embedded Development Board

## Slide 2: The heart of engineering isn’t calculation; It’s problem solving.
Schools may teach the numbers first, but calculation is neither the front end of engineering note its end goal. Calculation is one means among many to finding a solution that provides useful, objectively measurable improvement.

## Slide 3
Embedded Systems
Arduino Basics
Arduino Architecture
Arduino board layout. What are the resources available
Arduino IDE
Programming fundamentals
Learn by Doing – Sense, Control & Actuate
Project 1: LED Blinking
Project 2: RGB LED Interfacing & PWM Control
Project 3: Interfacing Sensors (Light, Temperature, etc.,)
Project 4: Interfacing Actuators (Motor Speed Control using PWM)
Introduction

## Slide 4: Industry / Robot / System
Industry / System

## Slide 5: System & Control
System / Plant: “A system may be a piece of equipment, perhaps just a set of machine parts functioning together, the purpose of which is to perform a particular operation”.
Control System: “A control system is an interconnection of components forming a system configuration that provide a desired system performance”

## Slide 6: Systems
Open loop systems
Closed loop systems

## Slide 7: Open loop system

## Slide 8: Closed loop system

## Slide 9: Multivariable control system

## Slide 10: Embedded Systems
"It is a combination of hardware and software to perform a specific task"
“An embedded system is a computer system with a dedicated function within a larger mechanical or electrical system, often with real-time computing constraints. It is embedded as part of a complete device often including hardware and mechanical parts. Embedded systems control many devices in common use today.”

## Slide 11: Components of Embedded Systems
Power Supply
Processor
Memory
Timers & Counters
Communication Ports
Input & Output
Application Specific Circuits
Software Components
Stable & Smooth Output
Proper Output Current to Drive the Load
Perfect Power Efficiency
Stable in Different Temperature Range
Proper Noise Filtering
Proper Decoupling
Line Regulation changes
Load Regulation – Fluctuation in output voltage when load current changes
Efficiency
Input/Output Ripple Voltage
Transient Response
Allowable Dissipation
Speed
Unit Price
Packaging
Performance
Peripheral Set
Timer on the Chip
Operating Voltage
Number of I/O Pins
Power Consumption
Amount of RAM and ROM
Specialized Processing Units
Architecture 8-bit, 16-bit, or 32-bit
Read-Only memory(RAM)
Random Access Memory(ROM)
Electrically Erasable Programmable Read-Only Memory (EEPROM)
UART
CAN
SPI
I2C
USB
Ethernet
RS-232
RS-423
RS-485
UART
I2C
SPI
Power Supply
Processor
Display Device
Buzzer for Alert
Device Drivers
MEMS devices
Assembler
Emulator
Debugger
Compiler

## Slide 12: a few points to remember…
ANALOG
DIGITAL

## Slide 13: Communication
PARALLEL
SERIAL
Sender
Receiver
1011000

## Slide 14: Pulse Width Modulation

## Slide 15: Pulse Width Modulation

## Slide 16: Why Arduino..?

## Slide 17: Lets Start Arduino…!

## Slide 18: Arduino Basics
arduino ( arrr-dween-oh )
(n.) It's an open-source physical computing platform based on a simple microcontroller board, and a development environment for writing software for the board.

## Slide 19: Types of Arduino Boards
Arduino Nano
Arduino Mega
Arduino LilyPad
Arduino Mini
Arduino Leonardo
Arduino Uno

## Slide 20: Arduino Uno
Digital pins:
14 digital IO pins
6 are PWM pins (3, 5, 6, 9, 10, and 11).
Analog pins:
6 analog pins(A0, A1, A2, A3, A4, and A5)
Takes analog values as an input

## Slide 22: Arduino IDE
VERIFY
UPLOAD
NEW TAB
OPEN
SAVE
SERIAL MONITOR
BOARD & SERIAL PORT SELECTIONS
CODE GOES HERE

## Slide 23: Basic Coding structure

## Slide 24: Basic Coding structure
setup() function
Called when a sketch starts.
To initialize variables, pin modes, start using libraries, etc.
Will only run once, after each power-up or reset of the Arduino board.
loop() function
Loops consecutively.
Code in the loop() section of the sketch is used to actively control the Arduino board.
Commenting
Any line that starts with two slashes (//) will not be read by the compiler, so you can write anything you want after it.

## Slide 25
pinMode()
Instruction used to set the mode (INPUT or OUTPUT) in which we are going to use a pin.
Eg: pinMode (13, OUTPUT);
ie. setting pin13 as output.
digitalWrite()
Write a HIGH or a LOW value to a digital pin.
Eg: digitalWrite (11, HIGH);
ie. setting pin 11 to high.

## Slide 26
digitalRead()
Reads the value from a specified digital pin, either HIGH or LOW
Eg: int inPin=7;
  val = digitalRead(inPin);
ie. reads the value from inPin and assigns it to val.
delay()
Pauses the program for the amount of time (in milliseconds) specified as parameter.
Eg: delay(1000);
ie. waits for a second (1000 ms = 1 s)

## Slide 27
Component List
Arduino Uno
USB cable
LED, RGB LED
LDR
POT(10k)
Resistors
Temp sensor LM-35
Motor Driver L293D, DC Motor
Connecting wire

## Slide 28: LED Blink

## Slide 29: Digital Read

## Slide 30: Analog Read

## Slide 31
LDR (Light Dependent Resistor)

## Slide 32
LDR - Wiring

## Slide 33: TEMP Sensor-LM35

## Slide 35: Motor Driver Circuit (L293D)
The L293 and L293D devices are quadruple high
current half-H drivers.
Output Current of 600 mA per channel for L293D)
DC Motor Drive – L293D

## Slide 36: L293D Functional Block Diagram

## Slide 38: DC Motor Control using L293D

## Slide 39: RGB LED
Vcc
Green
Blue
Red

## Slide 40: “How much more Arduino can do is only left to your imagination”

## Slide 41: Thank you